## Slide 1
RC Car for the Visually Impaired and the Deaf
ICARUS
Kyeongbuk Science High School

## Slide 2
Motivation
Recently, many companies are developing self-driving cars. As this is a technology that is emerging these days, we think it is worth considering to make products using the technology.
We had thought what I can make with self-driving technology, we finally decided to develop a technology that could help the handicapped.

## Slide 3
Outline
Launching Object Detection through OpenCV of information entered in Pi Camera.
Determine the driving judgment and driving strategy through CNN and RNN and create the driving path based on the driving strategy determined.
Transmits artificial intelligence into RC cars through Wi-Fi communication and implements vehicle control based on this decision.

## Slide 4
Effects of the Development
If this robot is developed, visually impaired people can communicate with the world.
It facilitates the walking of visually impaired people and hearing impaired people.
It reduces the possibility of accidents in the event of emergency for people with hearing and hearing impairments.
.

## Slide 5
Distinction
장애인들을 돕기 위한 기존의 제품들은 사용자가 어떤 장애를 가지고 있는지에 따라 별도의 제품을 사용해야만 했던 반면, 우리의 도우미 RC카는 시각, 청각의 구별 없이 시각장애인과 청각장애인에게 도움을 줄 수 있는 기능을 동시에 가지고 있어 범용성이 높다.
기존의 여러 제품에 적용된 기술들, 예를 들면 음성인식이나 TTS에 비해 최근 연구되기 시작한 자율주행 기술을 적용하여 장애인들의 생활을 보다 편리하게 해줄 수 있다는 점이 특징적이다.

## Slide 6
Assignment
Moonjae Kang: Configuring Raspberry Pi for the RC car, Writing the codes for
controlling the RC car
Mooseon Kim: Writing the codes for neural networks, Re-assembling the RC car
Seokjun Kim: Taking pictures, Writing the report
Juneseo Lee: Managing our GitHub, Preparing presentation slides

## Slide 7
Hardware Component
AlphaBot 3
Camera rotation
Uses two 3.4V lithium ion batteries
Why we selected this: It supports many programs by mounting Raspberry Pi

## Slide 8
Hardware Component
Range Rover RC Car
Size: 34cm 15.16cm 12.43cm
The main body uses AA batteries and the controller uses 9V batteries.
The frequency is 40 Hz and the controlling distance is 7-10 meters.

## Slide 9
Reasons for Changing Hardware
Attempted to use AlphaBot for price and efficiency, and for linkages with Raspberry Pi.
However, the RPM of both wheels was different, so we bought new hardware.
It was decided to use RC cars because they had excellent directional switching and propulsion compared to kit products.

## Slide 10
Hardware Component
RPi Camera (B)
Raspberry Pi Camera (B) Rev 2.0 with 1/4 inch 5MP OV5647 sensor is used. This camera can produce up to 1080p of images.

## Slide 11
Hardware Component
Raspberry Pi 3 model B
CPU: 1.2GHz ARM Cortex-A53 MP4
RAM: 1 GB LPDDR2
Price: $35.00
Reason for selection: Arduino was initially considered, but this was chosen instead of Arduino because the Raspberry Pi provides a more convenient use of the WiFi function and provides more diverse functions than the Arduino one.

## Slide 12
Tools Used
1. Python
1-1. Tensorflow
1-2. TFLearn
1-3. Numpy
1-4. OpenCV
2. SSH
2-1. PuTTY
2-2. Terminal
3. VNC

## Slide 13
Operating Environment
Programming Language: Python
Server PC: Windows
Raspberry Pi: Raspbian

## Slide 14
Sequences of the Development
0: Getting various guidance from Professor Yoon Eun-young of Computer
Engineering through R&E
1: Test basic operation of RC cars with raspberry pi
2: Development of Self-driving artificial intelligence using RNN and CNN
3: Label data for self-driving AI learning
4: Self-driving artificial intelligence using the above data
5: Implementation of self-driving technology through communication between
RC car and TCP server using Wi-Fi
6: Self-driving test of RC car after basic course construction

## Slide 15
Algorithm
The server PC collects training data by human’s controlling the RC car with the keyboard.
The server receives visual data from Raspberry Pi via network socket.
The server runs artificial neural networks such as CNN, RNN, FC, so that it can determine the direction where the RC Car will go.
Raspberry Pi receives the direction data from the server via network, and it automatically steers the motors.

## Slide 16
Flowchart
Raspberry Pi
Server PC
Socket
(Python)
Camera
Motor
Router A
Router B

## Slide 17
Flowchart
Raspberry Pi
Server PC
Socket
(Python)
Camera
Motor
Router A
Router B

## Slide 18
Project Diagram
Raspberry Pi
CNN, RNN
Server
RC car

## Slide 19
Data Labeling
Control the car along the rode model with a keyboard via network
Pi camera가 실시간으로 사진을 찍고 이미지를 픽셀로 변환
당시 RC카의 주행방향 정보(키보드 : 앞, 뒤, 왼, 오)와 함께
행렬 데이터로 저장
레이블 된 데이터 생성

## Slide 20
Learning Algorithm
Supervised Learning
: Learning a function that maps an input to an output based on example input-
output pairs
End-to-end Learning

## Slide 21
Development method
C, C++, Python등의 기초적인 프로그래밍 지식 습득
컴퓨터 비전에 대한 기본적인 이해
인공 신경망에 대한 기초적인 지식 습득

## Slide 22
How to use
1. RC카 전원을 켠다.
2. 인식할 수 있는 도로에 배치 한다.
3. 자율주행 하는 차량으로 부터 도움을 받는다.

## Slide 23
Demo
AlphaBot 3: Infrared Line Tracking - https://youtu.be/5Nc4KturL-U

## Slide 24
PROCESS
OF OUR
PROJECT
START
도우미 로봇은..
시청각장애인들의 보행에 도움을 주는 자율주행 로봇이다.

## Slide 25
START
PROJECT
Receiving Camera Data
The server PC receives camera data from Raspberry Pi via network
Network Socket
We used network sockets on Python for the communication between the server PC and Raspberry Pi

## Slide 26
START
PROJECT
Steering
Raspberry Pi receives the direction data from the server PC, and it autonomously steers the motors
Neural Network
The server pc runs some neural networks to determine the direction

## Slide 27
PROCESS
OF OUR
PROJECT
FINISH
자율주행
전달 받은 신호를 통하여 RC카의 자율주행 시행 및 이를 통하여 시청각장애인을 도움

## Slide 28
FINISH
OUR PRESENTATION THANK YOU